## Slide 1
Peter Boers
Next Level Orchestration voor SURFnet∞

## Slide 2: > whoami
Peter Boers 36 years old 9 years at SURF Background in Software and Network (SNE @ UvA) Started as a Trainee... …. moved on as Technical Product Manager A&O Tech lead of the Workflow Orchestrator Programme

## Slide 3: > cat ~/.zsh_history
Programming languages: Python, React, Angular
Databases: Postgres, Mongo, MySQL, Redis
Streaming: Kafka, Risingwave
Platform: Kubernetes, ArgoCD, GitlabCI, Github
Opensource: Workflow Orchestrator Programme
Current focus: Influx, PyTorch, Snellius + ML, gNMI and SNMP (get rid of it ;))

## Slide 4: Automation -> Orchestration -> Intelligent Networks
Since 2018, SURF has been automating the network. Fully automated delivery of services with the arrival of SURFnet8 Results: +/- 30 thousand automated changes > 14 million automated tasks 5430 active services (from BGP to Interfaces) 550k downloads on PyPi from orchestrator-core Self-Service in the Network Dashboard Open source Software developed by SURF in use by 12 to 13 other coporations

## Slide 5: SURFnet8 -> SURFnet∞

## Slide 6: SURFnet8 -> SURFnet∞
Opportunity to revitalize the network and the software that controls it From the tender(s) it is possible to get a Multi Vendor/Multi-OS architecture Diversity and complexity are increasing
  Campus network offering
  TFT
Higher level of integration is required. Developments follow in rapid succession and the tools we use must grow with them

## Slide 7
Our ambition is to have an Intelligent Network capable of correctly assessing incidents and fixing them in real-time by using AI-Ops

## Slide 8: What is AI-Ops?

## Slide 9: Network evolution, not revolution
With the continued development of SURFnet8, there is an opportunity to work with new(er) technologies
Two strategies are emerging for AIOps
  Machine Learning
  LLM integration

## Slide 11: What's wrong with SNMP?
Simple Network Management Protocol
Originated in 1988 with RFC 1067
De basis of network monitoring
  Traps for alerting
  Polling for statistics
It's not so "Simple" anymore
MIBs are huge and often vendor specific
  SNMP polling requires a lot of resources of the device
  … low resolution
  Little to no development
Multivendor network
https://issnmpdeadyet.com/

## Slide 12: gNMI
Variant of Streaming Telemetry
Still very much in development– Internet Draft
Based on YANG models (xml)
More and better models available
  OpenConfig
  “Standardized across all vendors”
Based on modern protocols
  gRPC
High resolution of data Possibility to configure the router to push the telemetry. Simple data format (protobuf, JSON) Very efficient!

## Slide 13: gNMI

## Slide 14: gNMI
Pro’s
  No MIB XPATH selectors Modern Internet Protocols High resolution for low cost
Cons
  Still very much in development Vendor support Bandwidth usage Which “standard” is the actual standard?

## Slide 15: SNMP
gNMI

## Slide 16: Implementing AI-Ops - Approach
Managing high resolution telemetry is proving to be a difficult engineering challenge
Data engineering
  Managing a large volume of telemetry
Use case modelling
  BGP neighbour

## Slide 17: Real-time processing and correlation
gNMI
gNMIc
TSDB
Sanitization
BGP Correlator
ML Models
Proposers
Alerters
+/- 100k e/ps
+/- 5 tot 10k e/ps
Other Correlator
+/- 10 e/ps
events
Other Correlator
Other Correlator
Network

## Slide 18: Correlator Pipeline - anomaly detection
Peering is Established
No prefixes received
+/- 5 tot 10k e/ps
Correlators
Correlators
Correlators
Correlators
Correlators
Correlators
Correlators
Inference
Resolution of 1 minute
Anomaly detected?
Correlator
Anomaly correlated
ML Models
Resolution of 1 hour

## Slide 19: Can we detect this usecase?
Traffic re-routed towards IX’es due to change @Microsoft

## Slide 20: Building a model – Adopting MLOps
Highly scalable
  Easy to train
  Easy to run
What is the best type of model?
  LSTM vs Transformers
Adopting MLOps
  From model training to application deployment

## Slide 21: LSTM
Long Short-Term Memory
Often used in anomaly detection
Example:
  “The cat sat on the ____”
  Reads one word at a time and predicts “mat” based on context
Neural network well suited for timeseries prediction
Trained with context about time of day and day of the week

## Slide 22: Transformers
Reads an entire sequence at once and remembers key information
Example:
  “The cat sat on the mat, because it was tired.”
  Knows that “it” refers to ”the cat”
Faster than LSTM and scales better with large amount of data
Basis for Chat-GPT and other LLM’s
Not as easy to adapt to timeseries data

## Slide 23: Demo of the LSTM model
Real time analysis of a raw data stream
  Monitoring a single BGP neighbour
  Filling of prediction buffer – sliding window
  Predicting 15 seconds ahead
  Detecting an induced anomaly when Mean Squared Error is > 99th percentile
Shout out: Victor Vlugt and Duncan Kampert

## Slide 24: Demo

## Slide 26: Implementatie van LLM – RAG agent
Retrieval
Augmentation
Documents are fetched from a vector database where queries are embedded and used to search semantically
Retrieved documents are passed to an LLM as well as an instruction and some tools to further augment the result, minimizing hallucination
The LLM produces a response using the combined query and context. The answer is
written in natural language, aligned with the retrieved documents.
Generation

## Slide 27: Demo van de AI Agent
First prototype of a chat agent in the orchestrator:
OpenAI compatible
    Not dependent on ChatGPT Open source: https://workfloworchestrator.org/orchestrator-core The basis for further connection to other data sources.
Shout out: Rene Dohmen, Virge B.V en GÉANT

## Slide 28: Demo van de AI Agent
First prototype of a chat agent in the orchestrator:
OpenAI compatible
    Not dependent on ChatGPT Open source: https://workfloworchestrator.org/orchestrator-core The basis for further connection to other data sources.
Shout out: Rene Dohmen, Virge B.V en GÉANT

## Slide 29: LLM based search
First we wan’t to be able to search accross multiple data sources
  Trigram similarity
  Word similarity
  L2 vector distance
First version is available in orchestrator-core 4.5.0 and component library 6.0.0
  Docs show the use of local-embeddings

## Slide 30: LLM based search

## Slide 31: AI agent

## Slide 32: MCP
Model Context Protocol to integrate other services
  Agents kunnen met elkaar communiceren over hun capabilities
  Zabbix MCP server
  Splunk MCP server
  Influx MCP server
Can you tell me what happened to service XYZ last Monday at around 23:00?
Why is this interface on node Y down?

## Slide 33: Implementing tool calls
Resources are made available to the agent by implementing so-called tools
A tool is a function that receives a certain input and gives an ouput, very simlilar to a function
  The tool is exposed to the LLM by decribing it’s use in Natural language
The Agent will combine multiple tool calls to return the best result possible to the user.

## Slide 34: Are there any questions?
Scan QR code for Workflow Orchestrator resources
?
\
Source Code
Discord