## Slide 1: Maat – PIONIER Source of Truth
Tomasz Szewczyk
Poznańskie Centrum Superkomputerowo-Sieciowe
23rd SIG-NOC

## Slide 2: INFRASTRUCTURE
21 MANs including 5 HPC centers
Optical DWDM transmission based on own fibers
MPLS based packet network
Transmission interfaces
  10Gbps
  100Gbps
  400Gbps
  800Gbps
Environment

## Slide 3: INFRASTRUCTURE
Many different software and hardware platforms, even if they come from the same vendor
  JunOS
    MX304
      Juniper Trio6
  Junos EVO
    PTX10001-36MR
      Juniper Express4
    ACX 7100 series
      Broadcom Jericho2
    ACX 7024
      Broadcom Qumran-2U
Avoid mistakes for repetitive instances
Use valid(ated) configuration for given platform
Need for automation

## Slide 4: SERVICES
Wide set of services
  Internet access
  MPLS based
    Virtual networks (VRFs)
      Unicast
      Multicast
    Point to point circuits
      BGP based
      LDP based
    EVPN
Demanding users with different needs
Atomic development and deployment
Generic solution and tools for future development
Need for orchestration

## Slide 5: HOW IT WORKS
Resources and services modeling in Maat
  Describe resources and services
  Avoid data duplication
Workflows
  Collect user input
  Interact with Maat via REST API
    Read existing data
    Create new object
    Modify existing objects
  Control implementation on devices
Changelog

## Slide 6: RESOURCES AND SERVICES MODELING
TMF based resources and services models

## Slide 7: RESOURCES AND SERVICES MODELING
@type – Service
category
  l2.circuit
  l2.circuit.sap
serviceCharacteristic
  Parameters specific to service instance
references
  serviceRelationship
  resourceRelationshp
identifier
  Register for available identifiers (eg. virtual circuit id, vrf target etc)
Ethernet point to point circuits (E-LINE)

## Slide 8: RESOURCES AND SERVICES MODELING
@type – Service
category
  l2.evpn
  l2.evpn.bd
  l2.evpn.sap
serviceCharacteristic
  Parameters specific to service instance
references
  serviceRelationship
  resourceRelationshp
esi
  Ethernet segment identifiers
EVPN

## Slide 9: RESOURCES AND SERVICES MODELING
@type – Service
Category
  l3.vrf
  l3.vrf.sap
serviceCharacteristic
  Parameters specific to service instance
References
  serviceRelationship
  resourceRelationshp
protocol
  signaling protocol enabled for service instance (BGP, OSPF etc)
identifier
  Register for available identifiers (eg. Virtual circuit id, vrf target etc)
VRF

## Slide 10: RESOURCES AND SERVICES MODELING
Administrative (technical) purposes only
Quick browsing of database objects
Manual editing of selected objects
Fix missing entries or references for manually defined objects or properties on infrastructure
Maat GUI

## Slide 11: RESOURCES AND SERVICES MODELING
Resources and Services tabs
Category pane
Tabular list of objects
  Text search
  Filtering
  Property display selector
JSON object overview
Maat GUI
@type
category

## Slide 12: RESOURCES AND SERVICES MODELING
Object attributes overview and editing
Define new attributes
  Schema validation applied by Maat API
Dynamic links to referenced objects
Maat GUI

## Slide 13: RESOURCES AND SERVICES MODELING
Automatic creation of new references between objects
  “backward reference” (bref:) defined in Maat GUI
  Automatic reference (ref:) from target object created by Maat API
Maat GUI

## Slide 14: RESOURCES AND SERVICES MODELING
JSON format overview and editing
Maat GUI

## Slide 15: RESOURCES AND SERVICES MODELING
Boost single source of truth development
  Add (develop) new services and resources not yet supported by workflows
  Include emergency fixes or changes for services and resources which are not yet supported by workflows
  Allow “atomic” automation and orchestration approach
Maat GUI

## Slide 16: CHANGELOG
Maat EventListener

## Slide 17: CHANGELOG
Mattermost integration
Interface between Mattermost channel and Maat database
  Quick lookup for services, resources and parameters
  Errbot based

## Slide 18: WORKFLOWS
Generalized workflows for use across multiple networks
  PIONIER
  GP4L
GÉANT LSO
  configuration changes on devices (resources)
  Ansible playbooks
  Jinja templates
Apache Airflow and GEANT LSO

## Slide 19: WORKFLOWS
Predefined forms for specific workflows
Existing data retrived from Maat
  Devices
  Interfaces
  Identifiers
Data/information acquisition

## Slide 20: WORKFLOWS
Basing on Maat information verify if service is implementable on given set of resources
Update Maat database
Prepare inventory and set of parameters for LSO
Collect implementation resuls
Apache Airflow and GEANT LSO

## Slide 21: WORKFLOWS
Airflow Mattermost integration DAG
  LSO input
  LSO callback
Apache Airflow and GEANT LSO
Playbook name
vendor name
model name
SAP parameters
SAP referenced interface
service parameters
playbook command
ansible role

## Slide 22: SUMMARY
Maat / SSoT objects
  Resources – 1 400+
    1 300+ interface
    45 device.router
    50+ customer
  Services – 1 374
    ~370 l2.circuit
    2 l2.evpn
    2 l3.vrf
    50+ network.core.links
Airflow
  330+ DAG runs
  1930 task states
Usage statistics

## Slide 23: SUMMARY
New workflows development
  EVPN
    vlan-based
    vlan-bundle
    vlan-aware
  Network configuration consistency verification
  VRF
  Ingres bandwidth control on SAPs
    Maat UI ready
Enabling user roles and Maat object access filtering
  Development finished
  Lab testing phase
The use of LLM for advanced data search functionality and user interaction
Future works

## Slide 24
The scientific work is published for the realization of the international project co-financed by Polish Ministry of Science and Higher Education from financial resources of the programme entitled "PMW”