## Slide 1
Sustainable Working practices in Asiera
Andy Byrne - SIG Sustainability
April 2026

## Slide 2
The Sustainability Challenge for NRENs
What we have learned
What we are doing
Where we need help
What NRENs can do today

## Slide 4
NREN’s have a role to play
Cost, regulation, carbon targets, reputation
Energy Efficiency – do the same, by using less
Why this matters
Photo : Robert Hackett – Asiera
Glendalough, County Wicklow, Ireland
Today 22% of Irelands Electricity supply is consumed by Data Centres

## Slide 5
Aseira’s Co2 Emissions – Scope 1&2
Chart: HEAnet Co2 Emissions 2025
| Schools Sites | Primary Data Centres | Regional Points of Presence | Small Client Sites | Office | Secondary Data Centres | Azure | AWS | Travel Flights | Travel Train & Bus | Travel Taxi - Account | Travel Taxi - Expenses | Travel Milage
 | 0.44114 | 0.31171 | 0.13888 | 0.03745 | 0.033695 | 0.0079872 | 0.0001481 | 4.4429e-06 | 0.022194 | 0.0014662 | 0.00035729 | 0.0002763 | 0.0046947
673 Tonnes
96% Grid Electricity
Average Irish dairy farm produces approximately 606 tonnes of CO₂ equivalent annually.

## Slide 6
Household devices V’s Asiera Devices
60 Watts
1500 Watts
180 Watts
25 Watts 3,000 Devices !
300 Watts 20 Devices
2,700 Watts 4 Devices
12 Hours a Day ?
6 Hours a Day ?
2 Hours a Day ?
24 Hours a Day, 365 Days a Year !
1. Power
Power : watt (w)
1,000 watts
= 1 kilowatt (kW)
2. Energy
Energy = Power x Time
Energy is measured in hourly = kWh

## Slide 7
Core Routers
Single Juniper MX960 ~ 2,700 Watts
~24,000 KwHr a year
https://www.epa.gov/energy/greenhouse-gas-equivalencies-calculator#results
2.2 petrol powered passenger vehicles driven for one year
1.3 homes energy use for one year

## Slide 8
Electricity Strategy
Renewable Utility Provider
Use more efficient equipment
Have a target
Design Choices
  Retire, Consolidate, Virtualise, Move to Cloud
  Mean ambient temperature
  PUE Data Centers
……what else ?

## Slide 9
Parkwest
34 Racks
$$
Blanchardstown
58 Racks
$$$
Citywest
18 Racks
$$
HEAnet Data Centre Review

## Slide 10
Blanchardstown
Data Centre
X empty Rack
Least used % for space and power​
Activities scaled down
  Moodle, Hosting, Multimedia, Storage
Most expensive rental ​
Least client circuit connections​
Dedicated Room
~ €2.5M Rental Savings over 5 years

## Slide 11
Chart: 2025 HEAnet Co2 Emissions
673 Tonnes CO2
Chart: HEAnet Co2 Emissions 2025
| Schools Sites | Primary Data Centres | Regional Points of Presence | Small Client Sites | Office | Secondary Data Centres | Azure | AWS | Travel Flights | Travel Train & Bus | Travel Taxi - Account | Travel Taxi - Expenses | Travel Milage
 | 0.44114 | 0.31171 | 0.13888 | 0.03745 | 0.033695 | 0.0079872 | 0.0001481 | 4.4429e-06 | 0.022194 | 0.0014662 | 0.00035729 | 0.0002763 | 0.0046947

## Slide 12
Data Centre Consolidation Results
45 % Reduction of Electricity in Data Centres
Cost Savings (Per Year) ~€165,000
Co2 Emissions Savings (Per Year) ~170 Tonnes
26 Million cups of Tea !

## Slide 13
Consolidation in Data Centre
Co2 Emissions Savings (5Yr) : ~19 Tonnes
30 % Switch Utilisation
95 % Switch Utilisation
Equivalent of :
4 Homes Electricity for 1 year

## Slide 14
Network Upgrade Programme
39 x MX104
450 Watts
47 x ACX7024X
97 Watts
27 x ACX5048
354 Watts
20 x ACX5448
303 Watts
OLD KIT
New KIT
Co2 Emissions Savings (5Yr) : ~157 Tonnes
Equivalent of :
31 Homes Electricity for 1 year
29 Million cups of Tea !

## Slide 15
CPE Projects
192 x ACX2200
60G Throughput
60 Watts
192 x ACX7020 Device
100G Throughput
65 Watts
800 x SRX240
600Mb Throughput
150 Watts
800 x XXX Device
28 Gb Throughput
20 Watts
OLD KIT
New KIT
Electricity Savings (5 Years) : ~4.5M KWHr
Cost Savings (5 Years) : ~€1.1M
Co2 Emissions Savings (5Yr) : ~1,181 Tonnes
182 Million cups of Tea !

## Slide 16
Sample Project – Network Migration
Chart: Migrating from Old Network to New Network
| Year 1 | Year 2 | Year 3 | Year 4
Migrate in 2 years | 64854.6048 | 100484.496 | 100484.496 | 35629.8912
Migrate in 1 year | 64854.6048 | 100484.496 | 35629.8912 | 35629.8912
Migrate in 6 Months | 64854.6048 | 68057.1936 | 35629.8912 | 35629.8912
Old Network Consumed 64k KWHr a year
New Network Consumes 35k KWHr a year
 | Total KwHr
Migrate in 2 years | 301,453
Migrate in 1 year | 236,599
Migrate in 6 Months | 204,172

## Slide 17
eWaste & Waste
Option B:
Option A:
Option C:
Income Guaranteed
Shared Revenue
Incurs a Costs
Client Auction

## Slide 18
Sustainability Fund
STEM Education-Focused Employee Volunteering Organised by Volunteer Ireland

## Slide 19
Energy Efficiency in Networks

## Slide 20
www.juniper.net/content/dam/www/assets/sustainability/us/en/day-one-green-optimized-thermal-design.pdf

## Slide 21
In Conclusion
We need your help
Incorporate Sustainability into your working practices
  Design
  Procurement
  Measure & Report
Share ideas
Share Successes
Collaboration is key
sig-sustainability@lists.geant.org