## Slide 1: Quantum sensors:
Technologies, networks and interfaces.
Ksawery Mielczarek 30th June 2026
1st GEANT SIG-Quantum meeting

## Slide 2: What is a quantum sensor?
Quantum sensor utilizes quantum mechanical phenomena, such as quantum superposition, quantum entanglement, and quantum squeezing, to measure physical quantities. [https://en.wikipedia.org/wiki/Quantum_sensor]
Main platforms:
  clocks,
  magnetometers,
  gravimeters,
  gyroscopes,
  antennas.

## Slide 3: 01
Technologies

## Slide 4: 1.1 Atomic clocks
Quartz clocks Atomic clocks
https://www.fizyka.umk.pl/
https://en.wikipedia.org/wiki/Crystal_oscillator

## Slide 5: 1.1 Atomic clocks
Quartz clocks: ms-s stability over 1 day. Atomic clocks: <1 ps stability over 1 day.
https://www.fizyka.umk.pl/
https://en.wikipedia.org/wiki/Crystal_oscillator
Quantum advantage: 9 orders of magnitude

## Slide 6: 1.1 Atomic clocks
Applications:
fundamental for GNSS (every satellite has atomic clock onboard),
electric power grids control (monitor AC phase),
5G telecom antennas (synchronize stations to avoid interference),
high-frequency trading (avoid microsecond-scale clock drift),
telescope (VLBI) and radar synchronization,
altitude measurement with general relativity.
Black hole shot with EHT. Credits: NASA
[1] https://spie.org/news/atomic-clock-applications
[2] https://www.nist.gov/atomic-clocks

## Slide 7: 1.1 Atomic clocks
https://commons.wikimedia.org/wiki/File:Caesium_spectrum_visible.png
How does it work?

## Slide 8: 1.1 Atomic clocks
Infrared
How does it work?

## Slide 9: 1.1 Atomic clocks
Infrared
Terahertz
How does it work?

## Slide 10: 1.1 Atomic clocks
Infrared
Terahertz
Microwave
How does it work?

## Slide 11: 1.1 Atomic clocks
Infrared
Terahertz
Microwave
Radio
9 192 621 770 Hz
How does it work?
Tuning RF oscillator to an ultra-narrow spectral line.

## Slide 12: 1.2 Magnetometers
Applications:
detection of magnetic objects (e.g. submarines),
no-GNSS navigation,
geophysical surveying and mapping,
magnetic imaging of integrated circuit,
subcellular resolution imaging,
brain acticity monitoring (MEG).
Quantum advantange: sensitivity higher 3-6 orders of magnitude.
[1] https://opg.optica.org/optica/fulltext.cfm?uri=optica-12-12-2008
[2] https://www.nature.com/articles/s42254-023-00558-3
[3] https://www.pnisensor.com/quantum-magnetometry-vs-classical-magnetometry/

## Slide 13: 1.2 Magnetometers
Technologies :
atomic vapour magnetometers,
nitrogen-vacancy (NV) center magnetometers,
SQUIDs.
https://en.wikipedia.org/wiki/Zeeman_effect

## Slide 14: 1.2 Magnetometers
Technologies:
atomic vapour magnetometers,
nitrogen-vacancy (NV) center magnetometers,
SQUIDs.
https://en.wikipedia.org/wiki/Zeeman_effect
Buy an NV magnetometer from QANT or a SQUID magnetometer from MEGIN
[1] https://qant.com/wp-content/uploads/2023/11/231114-Magnetometer-Brochure.pdf
[2] https://megin.com/megmaps/

## Slide 15: 1.3 Atomic gravimeters
Applications:
no-GNSS navigation,
minerals and oil finding,
predicting volcanic eruptions (underground lava monitoring),
agriculture (soil humidity measurement, forest growth),
detecting submarines.
Quantum advantage: 3 orders of magnitude higher sensitivity.
[1] https://www.mdpi.com/2072-4292/16/14/2634
[2] https://www.nist.gov/quantum-information-science/quantum-sensing-explained/turning-atoms-waves-measure-gravity-and

## Slide 16: 1.3 Atomic gravimeters
[1] https://www.exail.com/product/quantum-gravimeters
[2] https://www.jpl.nasa.gov/news/nasa-aims-to-fly-first-quantum-sensor-for-gravity-measurements/
[3] https://www.exail.com/resources/customer-stories/a-year-long-field-campaign-on-mount-etna-to-prove-the-absolute-quantum-gravimeter-value-for-volcanology
[4] https://www.exail.com/news/three-exail-absolute-quantum-gravimeters-delivered-to-tenerife-for-advanced-volcano-monitoring
Commercial quantum gravimeter
from EXAIL

## Slide 17: 1.3 Atomic gravimeters
How: atomic interferometry, mixing of two laser-controled free-falling atom beams.
A. Peters et al., 2001, Metrologia, 38 25

## Slide 18: 1.4 Atomic gyroscopes
Application: navigation in the areas where no electronic or visible feedback is available (aircrafts, submarines, ships, missilies, drones).
[1] www.nist.gov/noac/technology/time-and-frequency/atomic-gyroscopes
[2] https://payloadspace.com/vector-atomic-deliv
[3] https://www.quantum-australia.com/use-cases/quantum-gyroscopes-for-navigation
[4] https://vectoratomic.com/#inertial_section

## Slide 19: 1.4 Atomic gyroscopes
Application: navigation in the areas where no electronic or visible feedback is available (aircrafts, submarines, ships, missilies, drones).
[1] www.nist.gov/noac/technology/time-and-frequency/atomic-gyroscopes
[2] https://payloadspace.com/vector-atomic-deliv
[3] https://www.quantum-australia.com/use-cases/quantum-gyroscopes-for-navigation
[4] https://vectoratomic.com/#inertial_section

## Slide 20: 1.4 Atomic gyroscopes
Application: navigation in the areas where no electronic or visible feedback is available (aircrafts, submarines, ships, missilies, drones).
[1] www.nist.gov/noac/technology/time-and-frequency/atomic-gyroscopes
[2] https://payloadspace.com/vector-atomic-deliv
[3] https://www.quantum-australia.com/use-cases/quantum-gyroscopes-for-navigation
[4] https://vectoratomic.com/#inertial_section

## Slide 21: 1.4 Atomic gyroscopes
How does it work?
A horizontal atom interferometer in which the atoms are launched with initial velocity.
Fang, J.; Qin, J. Advances in Atomic Gyroscopes: A View from Inertial Navigation Applications. Sensors 2012, 12, 6331-6346.

## Slide 22: 1.4 Atomic gyroscopes
How does it work?
A horizontal atom interferometer in which the atoms are launched with initial velocity.
Fang, J.; Qin, J. Advances in Atomic Gyroscopes: A View from Inertial Navigation Applications. Sensors 2012, 12, 6331-6346.
Alternative: Atomic spin gyroscope – less sensitive but compact.

## Slide 23: 1.5 Rydberg sensors (Quantum antennas)
Applications: very broadband (DC - THZ), compact antennas able to receive very strong and very weak signals.
How it works: Pump laser excites atoms to Rydberg states, which are sensitive to electromagnetic field. Incoming microwaves/RF change the transperency of the atomic vapour to the probing laser, detected by a photodiode
[1] https://www.nist.gov/quantum-information-science/giant-atoms-measuring-radiation
[2] https://www.rydbergtechnologies.com/products
[3] https://www.forbes.com/sites/moorinsights/2024/02/20/quantum-sensing-unleashed-how-rydberg-sensors-will-disrupt-telecom/
Atom radius

## Slide 24: 1.5 Rydberg sensors (Quantum antennas)
A quantum antenna with optical detection? Not exactly, typically one uses electronic reference for higher accuracy.
Recent major improvement: a fully-optical Rydberg sensor.
[1] https://www.nist.gov/quantum-information-science/giant-atoms-measuring-radiation
[2] https://www.rydbergtechnologies.com/products
[3] https://www.nature.com/articles/s41467-025-63951-9

## Slide 25: 1.5 Rydberg sensors (Quantum antennas)
[1] https://infleqtion.com/quantum-rf-receiver/
Buy a 3 MHz – 6 GHz quantum antenna from INFLEQTION.

## Slide 26: 02
Networks

## Slide 27: 2.1 Optical clocks networks
Should we?
Yes, to have common time reference.
Can we?
Definetely.
Do we?
Sure.

## Slide 28: 2.2 Magnetometers networks
Should we?
Yes, to monitor geomagnetic storms and Earth’s core activity.
Can we?
Yes.
Do we?
Yes.

## Slide 29: 2.3 Gravimeters networks
Should we?
Yes, to monitor geological activity and underground water resources.
Can we?
Yes.
Do we?
Yes.

## Slide 30: 2.4 Rydberg sensors networks
Should we?
Possibly, for triangulation of unknown radars, jammers and transmitters.
Can we?
Yes.
Do we?
Not yet.

## Slide 31: 2.5 Gyroscopes networks
Should we?
No?
Can we?
Yes.
Do we?
No.

## Slide 32: 03
Interfaces

## Slide 33: 3.0 Different platforms in quantum
NV diamonds
(magnetometers)
SQUIDs
(magnetometers)
Trapped ions
(optical clocks)
Rydberg atomic vapours
(quantum antennas)
Cold neutral atoms
(gravimeters)
Alkali atomic vapours
(atomic clocks)

## Slide 34: 3.0 Different platforms in quantum
NV diamonds
(magnetometers)
SQUIDs
(magnetometers)
Trapped ions
(optical clocks)
Rydberg atomic vapours
(quantum antennas)
Cold neutral atoms
(gravimeters)
Alkali atomic vapours
(atomic clocks)
Quantum sensors => Quantum memories & qubits

## Slide 35: 3.0 Different platforms in quantum
NV diamonds
(magnetometers)
SQUIDs
(magnetometers)
Trapped ions
(optical clocks)
Rydberg atomic vapours
(quantum antennas)
Cold neutral atoms
(gravimeters)
Alkali atomic vapours
(atomic clocks)
1 GHz electronic 10 MHz 5 MHz 1 MHz 100 MHz
Quantum sensors => Quantum memories & qubits
Approximate optical spectral bandwidth
0.5 ns electronic 50 ns 100 ns 500 ns 5 ns
Approximate pulse duration

## Slide 36: 3.1 Spatial analogy
Multi-mode fibres
50 μm
Single-mode fibres
5 μm
Electro-optic modulators
10 μm
Quantum dots
1 μm

## Slide 37: 3.1 Spatial analogy
Multi-mode fibres
50 μm
Single-mode fibres
5 μm
Electro-optic modulators
10 μm
Quantum dots
1 μm

## Slide 38: 3.2 Spatial analogy
The plane wave treats space and time symmetrically.

## Slide 39: 3.2 Spatial analogy
The plane wave treats space and time symmetrically.
A glass lens stretches (magnifies) light spatially.
A ’’time lens” stretches (magnifies) light temporally*.
*And compresses spectrally – check time-bandwidth product.

## Slide 40: 3.3 What is a time lens?
Spatial lens
(piece of glass + focal length)
Time lens
(EOP modulator + dispersion)
+ + + + + + + + + +
- - - - - - - - - - - - -
Pockels effect

## Slide 41: 3.3 What is a time lens?
Spatial lens
(piece of glass + focal length)
Time lens
(EOP modulator + dispersion)
Total refractive index (or spatial phase, to be precise) changes parabolically in space.
Total refractive index (or temporal phase, to be precise)
changes parabolically in time.
+ + + + + + + + + +
- - - - - - - - - - - - -
Pockels effect

## Slide 42: 3.4 Time lens – use cases
Time lens application:
Imaging entangled photons below detector resolution.
State of entangled photons:
*Time-correlated entangled photons from an SPDC source separated by 6 ps recorded with SNSPD detectors with 50 ps time jitter. Measured at QPL UW.

## Slide 43: 3.4 Time lens – use cases
Time lens application:
Compressing spectral bandwidth of 70 GHz to 170 MHz.

## Slide 44: Thank you!
Ksawery Mielczarek 30th June 2026
kmielczarek@man.poznan.pl
1st GEANT SIG-Quantum meeting