## Slide 1
ESFRI Roadmap 2026
From a National Time & Frequency Network, REFIMEVE,
to a European Research Infrastructure
Fibre-based Optical netwoRk for European Science and Technology
Christian Chardonnet, CNRS
head of REFIMEVE

## Slide 2
Coherent optical links
Performances of frequency comparison
The revolutions in the time and frequency domain
3 revolutions of frequency standards :
1/ laser cooling of atoms 2/ frequency combs 3/ advent of optical clocks: 10-17 – 10-18
Revolution in frequency comparisons:
Colerent optical link surpass GPS and TW methods by more than 4 orders of magnitude: 10-19 – 10-20
Coherent optical links
Progress of frequency standards with time

## Slide 3
TOULOUSE CNES – LCAR - LAAS
MARSEILLE PIIM
NICE OCA - GEOAZUR
BRAUNSCHWEIG
PTB
LILLE PHLAM - IRCICA
STRASBOURG
TEDDINGTON
NPL
NANCAY USN
BORDEAUX LP2N
Operational links
Future extensions
International links
City - Lab
N
100 km
LPL
Crossborder
TURIN
INRIM
BESANCON
FOTON
SHOM
CERN
FEMTO-ST
UTINAM
PARIS
14 LABS
GRENOBLE-MODANE
ESRF – LIPHY – IRAM -LSM
TO SWITZERLAND
AUSTRIA
POLAND
BRUSSELS
VIENNA
MUNCHEN
FOTON
REFIMEVE today
network of 5000 km of optical fibre pairs mainly shared with the data traffic of RENATER
30 French labs + CERN connected
connections to the DE, UK, IT NMIs

## Slide 4
FOREST Partners from 15 countries
AT, BE, CZ, DE, ES, FR, IE, IT, LT, LU, MT, NL, PL, SK, UK.
+ CERN + GEANT
+ Specific role of EURAMET

## Slide 5
Earthquake detection with an optical fibre
September 2022
Earthquake in Mexico
Comparison between « noise » on an optical link SYRTE-LPL and signal from a seismometer of EPOS-FR.
Signal correlation : 0,94.

## Slide 6
Length of the national T&F networks
and cross-border connections
STRUCTURE OF THE FOREST NETWORK |  |  | 
 | Length (km) | DF | DC
TOTAL | 29 369 | 18 767 | 10 602
National networks | 23 672 | 14540 | 9132
NMI cross-border connections | 2 404 | 934 | 1 470
GEANT cross-border connections | 3 293 | 3 293 | 0
DF: Dark fibre
DC: Dark channel

## Slide 7
Network | Length (km) | DF | DC
TOTAL | 29 369 | 18 767 | 10 602
AUSTRIA | 746 | 730 | 16
BELGIUM | 1 000 | 0 | 1 000
CZECH REPUBLIC | 2 148 | 1 090 | 1 058
GERMANY | 1 137 | 1 137 | 0
FRANCE | 5 214 | 29 | 5 185
IRELAND | 1 749 | 892 | 857
ITALY | 2 843 | 2 587 | 256
THE NETHERLANDS | 760 | 0 | 760
POLAND | 7 035 | 7 035 | 0
SLOVAKIA | 5 | 5 | 0
UNITED KINGDOM | 1 035 | 1 035 | 0
Cross-border | 5 697 | 4 227 | 1 470
Length of the national T&F networks
and cross-border connections
DF: Dark fibre
DC: Dark channel

## Slide 8
FOREST network: already larger than the highly competitive Chinese project

## Slide 9
Evolution with time of the number of end-users connected to national T&F networks

## Slide 10
Structure of the partners expected to sign the FOREST MOU
14 NRENs, National Research and Education Networks
12 NMIs, National Metrological Institutes
+ GEANT, consortium of the European NRENs
35-40 other institutions which play a significant role in Science using high performance time & frequency, quantum communication, fibre sensing

## Slide 11
Other expected letters of support of FOREST
CERN which will participate to the governance of FOREST (WR collaboration)
BIPM, Bureau International des Poids et Mesures
EURAMET, consortium of the NMIs
ESA, European Space Agency
Several European Research Infrastructures:
  ESRF, LOFAR, JIVE, IRAM, VIRGO, Einstein Telescope
  EPOS, EMSO

## Slide 12
Sustainability
Globally, FOREST is already sustainable.
Most of the national Time-Frequency networks are operational for years. Half of the cross-border connections are financed nationally for years.
The second-half of the cross-border connections is covered by the C-TFN GEANT project financed by EC.
Extension of these cross-border connections and long-term financial commitments will be sought under the FP10 programme
Joint Research Center (EC) is helping finding long-term solutions.

## Slide 13
Thank you for your attention !